# General configuration settings

## Wi-Fi:

Modem initialisation:

wait(15) connect get(CONNECT)

Connection command

ATDT87.239.22.152/4001

GPRS Modem (Telit)

Modem initialisation:

wait(30) send(ATZ) wait(1) send(ATZ) get(OK) wait(1) connect get(CONNECT)

wait(30) CTO(30) send(ATZ) wait(1) send(ATZ) get(OK) wait(1) connect get(CONNECT)

Connection command

AT#SD=1,0,4000,"ezilog.net"

# Modem Setup for TCP/IP - EziLog setup

### 0. Factory setup and interface mode

AT&F	Factory reset

AT#SELINT?	Should be 2

### 1. Set the the context number 1 parameters

AT+CGDCONT=1,"IP", APN-Name

AT+CGDCONT?	To test

| Mobile | Command | Tested |
| --- | --- | --- |
| GiffGaff | AT+CGDCONT=1,"IP","giffgaff.com" | OK 05/14 |
| Vodofone-alt | AT+CGDCONT=1,"IP","internet" | OK 05/14 |
| O2 | AT+CGDCONT=1,"IP","payandgo.o2.co.uk" | OK 05/14 |
| TEST | AT+CGDCONT? |  |

http://apn-settings.com/uk/vodafone-uk-apn-settings/

### 2. Set the Authentication parameters

AT#SGACT=1,1,Username, Password

| Vodofone | AT#SGACT=1,1,"","" |
| --- | --- |
| GiffGaff | AT#SGACT=1,1,"","" |
| O2 | AT#SGACT=1,1,"payandgo","password" |
| Vodofone-alt | AT#SGACT=1,1,"web","web" |
| TEST | AT#SGACT? |
| TEST | #SGACT: 1,1 |

Possible errors:

+CME ERROR: context already activated

- dont bother changing

### 3. Set the timing latency

AT#SCFG=1,1,0,90,600,2

Socket=1, PDP=1, Packet size=0=default, timeout=90s, 
	Connection timeout=600s, 	TxTimout=0.2s

AT#SCFG?

To test

### 4. Set automatic context activation on power on

AT#SGACTCFG=1,10,180,0

PDP=1, Retry=10, Delay=180seconds,

AT#SGACTCFG?

To Test

### 5. Save configuration

AT&W

### 6. Test connection

AT#SD=1,0,4000,"ezilog.net"	New Interface

AT#SKTD=0,4000,"ezilog.net"	Old interface

# Common problems

Socket hangs when testing port 80 web site

Ensure that line ends with CRLF (check hyperterminal settings)

Connection aborts half way though as if reset

Ensure that there is sufficient power to the modem

# Usefull diagnostic commands

at+cmee=2	Verbose mode

at+creg?	Check network

AT&V        	displays a list of current configuration

AT#SELINT   	Selected interface mode - should be 2 for new modems

AT&V1       	Register display

AT&V2       	Last connection status

at#csurv    	site survey

at#ceer     	error repor

ati4        	identification e.g. GC864-QUAD-V2

see also ati1..5  futher identification

at+cfun?    	should be 1